## Slide 1: WIND And Solar ENERGY CONVERSION MODEL GUIDELINES Consultation update – September 2016
26 September 2016
Presented by Marcelle Gannon

## Slide 2: SESSION OVERVIEW
    Status of Consultation Process
    Local Limit and Wind Speed Changes
    Extreme Wind Cut-out / Other Cut-out
    “Possible Power” / “Estimated Power” Proposal
    Next Steps

## Slide 3: Current STATUS of Consultation Process
Draft Report stated
  Local Limit and Wind Speed minor amendments
  “Possible Power” excluded
  Extreme-wind cut-out SCADA proposed
Stage | Date
Issues Paper | 18 March 2016
First stage submissions | 27 May 2016
Draft Report | 2 August 2016
Second stage submissions | 25 August 2016
Final report due (currently) | 7 October 2016
Strong participant feedback in second stage raised question whether AEMO should extend consultation to include new functionality – discussed in following slides

## Slide 4: Local Limit and Wind Speed
Local Limit SCADA signal resolved
  Small amendments following second stage consultation
  AEMO working on distribution network limit constraint equations
Wind Speed SCADA signal definition resolved

## Slide 5: Turbine cut-ouT
Draft report proposed new “Extreme wind cut-out” SCADA
  To improve accuracy of AWEFS dispatch forecast when wind farm constrained during extreme wind events
Feedback in submissions:
  May be expensive or difficult for some farms
  Many causes for cut-out or reduced production
Ideas for a signal to allow AWEFS to model more of this behaviour more accurately in dispatch?
  Turbines ready-to-run in next 5 minutes?
  Share of capacity ready-to-run in next 5 minutes?
AEMO needs some signal to represent what’s happening in times of cut-out

## Slide 6: “Estimated Power” proposal
Substantial participant feedback in second stage
“Estimated Power” name to avoid confusion with existing “Possible Power” in control systems
Participants keen to provide a signal to incorporate all factors affecting wind farm operation, including:
  Wind speed / direction at each turbine
  Effects of high wind speed, extreme wind direction change, site temperature, wind sector management
  Dynamic effects of turbine pausing and feathering

## Slide 7: “Estimated Power” proposal
AEMO would analyse the accuracy of trial data supplied by participants – we need to work with you
AEMO would concurrently consult with participants
Regular reporting back with full transparency on outcomes
  If it meets requirements for system security and market outcomes, should we then implement “Estimated Power”?
  If it doesn’t meet requirements, should we then require the high-wind cut-out signal or an alternative cut-out signal?
Post-implementation
  AEMO would continue to measure performance and assess reliability

## Slide 8: Proposed “Estimated Power” Definition
Optional SCADA signal
  The Generator’s forecast of active power at the end of the next dispatch interval
  Subject only to technical factors affecting operation of its generation and connection assets
  Calculated assuming no distribution or transmission network constraints apply to the next dispatch interval

## Slide 9: “Estimated Power” proposal
Q: How much detail to put in the definition?
Q: Overlap with the “Local Limit”?
Q: Useful for your farm, or too complex?
Q: Also for solar farms?

## Slide 10: Next Steps for current consultation
Next report published 14 Oct 2016
    A week delayed to incorporate the complexity of the issues raised in the second stage submissions and discussions.
Two Options:
  1 – End consultation now, with “Estimated Power” not in ECM Guidelines
  2 – Third round of consultation, to propose “Estimated Power” in ECM Guidelines

## Slide 11: Next Steps for current consultation
“Estimated Power” accuracy assessment
  Accuracy assessment can start now using SCADA and historical data under Option 1 or 2
Local Limit
  Option 1: Implementation work can commence from October
  Option 2: Implementation delayed, though background work will minimise delay
“Estimated Power”
  Option 1: New full consultation would be required to put “Estimated Power” into ECM Guidelines – minimum 4 months
  Option 2: Could allow proposals with respect to “Estimated Power” to be implemented without new full consultation
Question: Which option is preferred?

## Slide 12: Next Steps for current consultation
Timeline if a third stage of consultation was undertaken
Stage | Date
AEMO second draft report published | 14 October 2016
Third stage stakeholder submissions due | 4 November 2016
AEMO final consultation report published | 9 December 2016

## Slide 13: Additional consultation and investigation underway/proposed
Power curve tuning
  AEMO has been working with AWEFS vendor to improve the power curve tuning algorithm
  Design improvements in final stage of negotiation
Scoping of a full review of AWEFS
  Continuing investigation into accuracy improvements to AWEFS other than Estimated Power
Transparency and Bidding of Availability