## Slide 1: 5MS Joint Metering/Systems Focus Group
Friday, 14 September 2018
AEMO Office:
Level 22, 530 Collins Street, Melbourne

## Slide 2: Agenda
NO |  | Time | AGENDA ITEM | Responsible
Preliminary Matters |  |  |  | 
1 | 9:30am – 9:40am | 9:30am – 9:40am | Welcome, introduction and apologies | Emily Brodie (AEMO)
Matters for Noting |  |  |  | 
2 | 9:40am – 9:50am |  | AEMO’s profiling of 15 and 30-minute data | David Ripper (AEMO)
3 | 9:50am – 10:00am |  | Unit of measure precision | Hamish McNeish (AEMO)
4 | 10:00am – 10:10am |  | AEMO use of B2M (MDFF format) | Hamish McNeish (AEMO)
5 | 10:10am – 10:20am |  | Extending NEM12 to include 5-minute data | David Ripper (AEMO)
 | 10:20am – 10:30am |  | Break | 
Matters for Discussion |  |  |  | 
6 | 10:30am – 11:00am |  | Accepting non-settlement data | Hamish McNeish (AEMO)
7 | 11:00am – 1:00pm (includes lunch break) |  | Transition to 5-minute meter data AEMO program schedule Aggregating and profiling metering data How will participants deal with metering data during transition Develop high level milestones for key activities | David Ripper and Hamish McNeish (AEMO)
8 | 1:00pm – 1:30pm |  | File size and communications capabilities | Feedback from participants
Other business |  |  |  | 
9 | 1:30pm – 1:50pm |  | General questions | David Ripper and Hamish McNeish (AEMO)
10 | 1:50pm – 2:00pm |  | Next steps | David Ripper and Hamish McNeish (AEMO)

## Slide 3: AEMO’s profiling of 15 and 30-minute data
David Ripper

## Slide 4: Profiling of 15 and 30-minute meter data
Question
How will AEMO undertake profiling?
Outcome
AEMO will profile from 15 minute to 5 minute and 30 minute to 5 minute using a percentage allocation method
The profiling at the moment is at the profile area
If Global Settlement drives changes then we will take this into account

## Slide 5: Profiling – percentage allocation method
Example
5 minute trading interval (TI) | 1 | 2 | 3 | 4 | 5 | 6 | Total for 30 minutes
Wholesale feeder TI values | 100 | 150 | 120 | 150 | 230 | 250 | 1000
TI value % of 30 minute total | 10% | 15% | 12% | 15% | 23% | 25% | 100%
Corresponding 30 minute TI | 10 |  |  |  |  |  | 
5 minute trading interval (TI) | 1 | 2 | 3 | 4 | 5 | 6 | Total for 30 minutes
30 minute TI profiled to 5 minute | 10 x 10% | 10 x 15% | 10 x 12% | 10 x 15% | 10 x 23% | 10 x 25% | 
5-minute profile values | 1 | 1.5 | 1.2 | 1.5 | 2.3 | 2.5 | 10

## Slide 6: Unit of measure precision
Hamish McNeish

## Slide 7: Precision of kWh Meter Reads
Question
A concern was raised on possible loss of precision if AEMO stores meter reads in kWh. For example receiving a value of 3.2 Watt-hours.
Outcome
MDFF NEM12 and NEM13 formats currently define support to 1 Wh precision.
MDMF support is assumed to be the same – but the format is not explicit
AEMO could support to 4 decimal places and update the formats
AEMO’s systems would convert received meter reads to kWh supporting up to 4 decimal places
AEMO’s systems would accept Wh, kWh, MWh, and the stored value would be to 4 decimal places in kWh, rounding would occur if required.
Other units of measure will be treated consistently, such as for vars

## Slide 8: AEMO use of B2M (MDFF)
Hamish McNeish

## Slide 9: To-Be Process – MDFF delivery
Green is existing and unchanged, Orange is new
MDFF will be accepted over web API’s and FTP

## Slide 10: MDFF vs MDMF
Supporting of 5 minute meter data
  MDFF - Supports different intervals in the format
  MDMF - Does not support different intervals – required to be 30-minute
Options:
  Option A: Use MDMF – change format and/or add interval to standing data
  Option B: Use MDFF – already supports 5 minute
Current SWG and PWG discussion supported Option B.

## Slide 11: Meter Data over B2B and B2M
Data Formats will unify to MDFF
Participants may use MDMF to send interval reads (N1 or signed E1/B1 etc) @ 30-min resolution (or) consumption for Basic meters
Participants may use MDFF to send interval reads (E1, E2, B1, K1, Q1 etc) @ 5-min or 15-min or 30-min resolution (or) consumption for Basic meters
Validation:
  PMD/VMD B2B processes remain unchanged
  For B2M meter data AEMO proposes to periodically run the RM11 report to inform MDP’s of missing meter reads
  RM11 could be delivered prior to 1 July 2020. Is this wanted? And when?

## Slide 12: Extending NEM12 to include 5-minute data
David Ripper

## Slide 13: NEM12 to include 5-minute data
No comments received on needing an additional data format
NEM12 format can support 5-minute data with out a format change
Interval length to remain in 200 record
The MDFF document will be updated with how the 5-minute reads will be represented
Changes identified in the HLIA
  Add in AEMO to list of parties to receive MDFF
  Interval metering data – add 5-minute data to section 3.3.3.
  Define 5 minute start and end times.
  Remove MDM and net data file references.
  Produce example of 5 minute file.
    300 record [288 interval values for 5 minute, 96 interval values for 15 minute, 48 interval values for 30 minute]

## Slide 14: Proposed NEM12 Examples
Current 300 record
300,20040201,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,1.111,A,,,20040202120025,20040202142516
Proposed 300 record
300,20040201,[288 interval values for 5 minute, 96 interval values for 15 minute, 48 interval values for 30 minute],A,,,20040202120025,20040202142516

## Slide 15: Accepting non-settlement data
Hamish McNeish

## Slide 16: Non-settlement data
With a view of future-proofing AEMO will add capability to handle accepting non-energy settlement streams. So if this data is provided in MDFF and registered in standing data then AEMO’s systems will support this. On the horizon:
  3rd Party Access to Data (Customer Data Right)
  Settling Virtual Power Plants
  Support of Distributed Energy Resources (DER) services
The MDM will need to determine which data streams provided via MDMF/MDFF will be accepted, validated, made available and used in settlement.

## Slide 17: Data streams treatment – UOM and sign
The MDM requires a means to determine the unit of measure of received meter data:
  Option 1: Use MDFF Record 200 – validate UOM is of a known type. Data streams via MDMF received data are always in kWh.
  Option 2: Addition to standing data (CNDS), and validate that the NEM12/13 content matches this.
The MDM requires a means to identify if the usage sent in MDFF should be treated as a positive or negative: (MDMF is always signed)
  Option 1: Using the first character of data stream suffix (e.g. ‘E’ is Export, ‘B’ is Import etc)
  Option 2: New attribute to indicate whether the data stream (or register) is Import (B1) or Export (E1) or Signed (N1) in CNDS

## Slide 18: Data streams treatment – accepting
With receipt of additional data streams (non-settlement) how should this be registered?
  Option 1: Only settlement data streams are registered in CNDS
  Option 2: All data streams are registered in CNDS and validated, a new field indicates those to be used in settlement
  Option 3: Use other existing attributes of CNDS, like Data stream Type, First character of suffix etc
Related to Option 2, there is the possibility of AEMO receiving of meter data for a data stream that isn’t currently registered and waiting a period of time for the data stream to be registered, and to then load that parked metering data.
  If not resolved in X (3?) days then the read becomes invalid and would be rejected
  These “missing” reads would not show up in the RM11 since the data stream has not been defined
  A new report may be required to highlight these reads in a parked state in need of a data stream definition

## Slide 19: Transition to 5-minute data
David Ripper and Hamish McNeish

## Slide 20: AEMO program schedule
AEMO accepts MDFF files from 1 July 2020 – and will settle with these
AEMO expects participant to send either MDMF or MDFF for a data stream – not both
Only MDMF retrospective net reads will be accepted from 1 July 2022
MDMF format will no longer be accepted after 1 July 2023
Participants have a 3 year period from 1 July 2020 to transition from MDMF to MDFF (noting only retrospective reads supported in the last year)

## Slide 21: Aggregating and profiling metering data
Before 1 July 2020 – MDPs will need to aggregate 5 and 15 minute to 30 minute and provide in MDMF format to AEMO for settlement
Before 1 July 2020 – Participants and MDPs may choose to exchange new 5 and 15 minute data via B2B
From 1 July 2020 – 5 and 15 minute reads received by AEMO will be aggregated by AEMO to 30 minutes and settled
From 1 July 2021 AEMO will profile received 30 and 15 minute reads to 5 minute resolution
From 1 July 2022 AEMO will only accept retrospective reads via MDMF files
From 1 July 2023 AEMO will reject or ignore any received MDMF files

## Slide 22: How will participants deal with metering data during transition?
AEMO will support MDMF for a 2 year window after 1 July 2021
Participants will need to manage the handling of different resolution data and formats (from MDPs) during the transition periods.
Participants may have additional data stream standing data (CNDS) to provide/modify when 5 minute support is introduced
Metering data delivered via B2B and delivery of metering data to AEMO (MDMF and MDFF) are independent
If a newer version of meter data exists it is required to be delivered to participants and AEMO

## Slide 23: Develop high level milestones for key activities
Activity:
  Group discussion and whiteboard use to identify key milestones
Proposed Areas to Cover:
  Timeframe 1 Dec 2019 to 1 Jul 2023
  Approx. 23,500 meters to transition by 1 July 2021 (Type 1,2,3,7, subset of Type 4)
  New and replacement meters
    From Dec-18, any new or replacement meters other than Type 4A must be 5 minute capable
    From Dec-19, any new or replacement Type 4A must be 5 minute capable
    By Dec-22, all meters installed under 1. and 2. above must be producing 5 minute data
  Meter reconfiguration program
  CATS aseXML schema/standing data
  Meter data sending/receipt capability
  Participant types: MDPs, AEMO, DBs, Retailers, MC, MPB
Outcomes:
  Proposed high-level milestone dates

## Slide 24: File size and communications capabilities
Hamish McNeish

## Slide 25: 1 MB Message File size
Reduce overall growth in number of files
There is support in the SWG and PWG to increase the current B2B and B2M 1 MB message content (uncompressed) limit.
AEMO is assessing:
  What we believe our systems and networking can cope with and maintain service levels
  Review current archiving services of messages (with 13 months online currently)
Due to the increase in received data (regardless of the 1 MB limit) AEMO is assessing:
  The potential need to increase bandwidth allocations, and AEMO’s network infrastructure
  Costs of bandwidth allocations
Questions
Do participants support increasing for both B2B and B2M?
What are attendees system constraints?
What size should we increase to? 5/10/X MB has been proposed as a possible target

## Slide 26: General questions
David Ripper and Hamish McNeish

## Slide 27: Next steps
David Ripper

## Slide 28: Next steps – procedures consultation
Consultation will proceed for metering data package of procedures
Procedure Title | Consultable Procedure | Impact
MDFF Specification NEM12 and NEM13 | N | High
MSATS Procedure: Metering Data Management (MDM) Procedure | Y | High
MDM File Format and Load Process | N | Medium
Metrology Procedure: Part A | Y | High
Metrology Procedure: Part B | Y | High
Retail Electricity Market Glossary and Framework | Y | High